## Slide 1: .
.
Brain-Computer Interfaces
In Quadriplegic Patients

## Slide 2
.
. | .
Sara Anis Halim | 18003
Ahmed Gaber Rhouma | 18044
Omar El-Sool | 18183
Amira Hisham Momen | 18194
Ibrahim Ayman Abu-Shara | 18011
Hazem Akram | 18127
Mohamed El-Bordiny | 18068
Our Team
Name
ID

## Slide 3
.
The project
Human brain
Streaming Data
Server
Decision
(Normal , forward,
right , left)
MC
Control
Wheelchair Prototype
Signal processing
Split
blinks
ML

## Slide 4
S-EEG Sensor
Human brain
Streaming Data
Server

## Slide 5: EEG Sensor
Planet Mercury is the closest object to the Sun
Mercury
Mars
Despite being red, Mars is a cold place
Jupiter
Jupiter is a gas giant and the biggest planet
(electroencephalography)
It is a test used to evaluate the electrical activity in the brain.
Brain cells communicate with each other through electrical impulses.
Scalp EEG recording displays the difference in electrical potentials between two different sites on the head

## Slide 6: EEG compared to other brain imaging techniques

## Slide 7: EEG Advantages
Choose EEG techniques despite the existence of better devices than other techniques.

## Slide 8: The Brain and Biological Neural Network
Action potential
03
The billions of neurons in the human brain have highly complex firing patterns
Every interaction between these active neurons creates a minimal electrical discharge, which creates different amplitude and frequencies
02
01

## Slide 9: The Ten-Twenty System
The international ten-twenty System of Electrode Placement uses on the Scalp to take signal.
It begin with one or two letters indicating to the general brain region
Each Channel name begin
It is ended by the numbers that indicating the distance between channel and middle of the brain
Each Channel name end

## Slide 10: Muse & S-EEG Sensor
Muse
01
S-EEG Sensor
02

## Slide 11: Muse Headset
01
02
03
04
Muse based on EEG Technique
Muse advantages & disadvantages
Muse Channels
Channels locations

## Slide 12
S-EEG Sensor
S-EEG Sensor channel TP10, FPZ
S-EEG Sensor Advantages
S-EEG Sensor output

## Slide 13: Sensor Components
Notch Filter
To block 50 Hz
amplifer
Because the signal is very small in mv
Filters
Because the signals is very noisy.
To deal with the signal
ADC
01
02
03
04

## Slide 14: Input & output of each step
Continuous analogy electrical signal
Filters
ADC
Electrical waves
Amplifition Electrical signal
Signal is amplifiered and filtered
After ADC, analogy signal convert to Digital values
Electrodes
Electrical
Waves from
brain
Electrical waves in mv
Amplifier
amplification Electrical signal
Must be in range to pass

## Slide 15: Electrodes
01
02

## Slide 16: Amplifier
The instrumentation Amplifier that is extension of the difference amplifier (amplifies the difference between its input signals)
The Final Output of instrumentation Amplifier

## Slide 17: Filters
02
01
Band Pass Filter:
To control in range that we need
From 1.5 hz to 318 hz
Notch Filter:
To block 50 Hz from our frequencies band

## Slide 18: Filter(Band Pass Filter)
The Final Output of Band pass Filter
Band Pass Filter is used to detect range that we need From 1.5 HZ to 318 HZ

## Slide 19: Notch Filter
The Final Output of Notch Filter
Notch Filter used to block 50 HZ

## Slide 20: Design Implementation
02
01
BreadBroad
PCB

## Slide 21: BreadBroad:
02
01

## Slide 22: The output of S-EEG Sensor
The output of eyes blink
TP10
FPZ

## Slide 23
The Design of PCB and The rooting of PCB
Proteus design
01
02
Proteus design

## Slide 24
PCB
03

## Slide 25: ADC
ADC
it uses to convert the analogy continuous electrical signal to digital to enable us to use it and deal with signals coming from the brain.
numbers

## Slide 26
Signal
Processing
Streaming Data
Server
Signal processing

## Slide 27
.
Analysis
Pattern Recognition
Real Time Intelligent Control System
Raw Data
Signal Processing

## Slide 28
Requirements And Design
0
Signal Processing

## Slide 29: Requirements
Search & Connect
01
make dynamic threshold
04
02
03
Graph the microvolts data for 4 channels
Record data for
machine learning

## Slide 30
GUI Design

## Slide 31
Interface

## Slide 32
Analysis For Blink Detection
0
Signal Processing

## Slide 33
Frequency Band

## Slide 34
Eyeblinks in microvolts
Microvolts data for blinking 12 times

## Slide 35
Frequency Domain Analysis
Frequency graph for the same data

## Slide 36
Adaptive Threshold
0
Signal Processing

## Slide 37
Unstable Delta
File 1
File 2
File 3
Peak: 5000
Peak : 8000
Peak : 7000

## Slide 38
Add New Section

## Slide 39
Dynamic Threshold

## Slide 40
Analysis
Pattern Recognition
Real Time Intelligent Control System
Raw Data
from Muse
0
Signal Processing

## Slide 41
Event-Related Potential
ERPs are those EEGs that directly measure the electrical response of the cortex to specific events.
Sensory
Motor : Related to (BCI )
ERP : large number of action potentials (APs) that are Time Locked.
0
Signal Processing

## Slide 42
Eyeblinks in microvolts
blinking for 12 times
Time (ms)
m volt
0
Signal Processing

## Slide 43
Signal Processing
Real Time Signal Processing
2 ) Event-Related Potential  Time locked
1 ) Brain Wave Classification  Frequency Domain Analysis ( DFT )
So , our system needs Time-Frequency Analysis ( STFT )
0
Signal Processing

## Slide 44: Short Time Fourier Transform
Signal Processing
New Parameters
- g(n) : Window Equation
- M : Window Length
- L : Overlapping Length
- R : Shift Length
Buffer equation :
(Buf_Length - Epoch_Length) / Shift_Length + 1
0
Signal Processing

## Slide 45: Computational aspects
DFT : for a signal with T points, this takes approximately arithmetical operations
Which will be slow with large T
So we will implement DFT using Fast Fourier Transform implementation
FFT Applying Divide and Conquer strategy , running in time approximately ( T log T )
which can result in huge savings in computation time
Signal Processing
0
Signal Processing

## Slide 46
Signal Processing
Real Time Control System
0
Signal Processing

## Slide 47
Wheelchair movement flowchart
0
Signal Processing

## Slide 48
Class Diagram
0
Signal Processing

## Slide 49
Sequence Diagram
0
Signal Processing

## Slide 50
Signal Processing
Real Time Intelligent Control System
0
Signal Processing

## Slide 51
Class Diagram
0
Signal Processing

## Slide 52
Eye Blinking
&
Automation
Human brain
Streaming Data
Server
Signal processing
Split
blinks

## Slide 53: 0
Artifacts
Artifact on EEG is anything that does not arise from the brain itself.
Electromyography(EMG)
Electrooculogram(EOG)
Types of artifacts:
Eye Blinking& Automation

## Slide 54: 0
Bell's Phenomenon
It describes the reflex upward movement of the front of the eyeball when the eye blink. Because the cornea is positive and the retina is negative , this causes a deflection .
Eye Blinking& Automation

## Slide 55: 0
Eye Blinking& Automation
Muse electrodes localization
localization has been one of the primary goals of solving the inverse problem in EEG. What this means is identifying where in the brain a particular type of activity originates based on the surface EEG recording.

## Slide 56: 0
Eye Blinking& Automation
Polarity Rules
Input 1 more positive than Input 2 and conversely that Input 2 more negative than Input 1 : upward deflection
Input 1 more negative than Input 2 and conversely that Input 2 more positive than Input 1: downward deflection
Input 1= Input 2: no deflection (flat line)

## Slide 57: 0
Eye Blinking& Automation
Apply Polarity Rules on Muse2
Time (s)
Volt (µv)
When the blink happens the signal's polarity is positive at the electrode to which the cornea is moving.

## Slide 58: 0
Eye Blinking& Automation
Electrodes classify type of blinks
Right Blink
Left blink
Double Blink
Double Blink
According to Muse electrodes localization and Polarity Rules:
AF7
AF8
TP9 or TP10
Right Blink
Left blink
Double Blink

## Slide 59: 0
Eye Blinking& Automation
Data For Machine learning
Why we do all of this ?
Recording data:
Desktop application (BHI Muse)

## Slide 60: Methods to record and split EOG data
Record and split by sound
Get EOG data by sound indicator
Desktop application Recorder
Generates a CSV File contains EEG data of 4 chanels
Record and split by threshold
Get EOG data by mathematical method
0
Eye Blinking& Automation

## Slide 61: 0
Eye Blinking& Automation
Record and split by threshold
mathematical method gets only blinks and discards anything else.
Time (s)
Volt (µv)

## Slide 62: 0
Eye Blinking& Automation
Steps to split:
Get the absolute :

## Slide 63: 0
Eye Blinking& Automation
Steps to split:
2. Clean the signal:

## Slide 64: 0
Eye Blinking& Automation
Steps to split:
3. Detect the threshold of eye blinks peeks:
In our first code we tried find the peek point using normal for loop
Then we found python library called Nerokit 2

## Slide 65: 0
Eye Blinking& Automation
Steps to split:
4. Get the original blink data :

## Slide 66: 0
Eye Blinking& Automation
2. Record and split by sound indicator
Big problem: threshold couldn’t recognize the pattern of blink because of EMG
Solution: 2 seconds sound as an indicator for the blink 1s close / 1s open

## Slide 67
Deep
Learning
Human brain
Streaming Data
Server
Signal processing
Split
blinks
ML
Decision
(Normal , forward , right , left)

## Slide 68: “Birds inspired us to fly, burdock plants inspired Velcro, and countless more inventions were inspired by nature. It seems only logical, then, to look at the brain’s architecture for inspiration on how to build an intelligent machine.”
—Aurelien Geron
Planet Mercury is the closest object to the Sun
Mercury
Mars
Despite being red, Mars is a cold place
Jupiter
Jupiter is a gas giant and the biggest planet

## Slide 69: Motovation 01 Pre-processing 02 Filtering 03 Modeling 04 Deployment 05 Table Of Contents

## Slide 70: Preprocessing & Filtering 02

## Slide 71: Savitzky-Golay Filter
0
Deep Learning

## Slide 72: From Raw Data to Row Data
0
Deep Learning

## Slide 73
0
Deep Learning

## Slide 74
0
Deep Learning

## Slide 75
0
Deep Learning

## Slide 76: Modeling 03

## Slide 77: Double Eye Blinking Classification
0
Deep Learning

## Slide 78: Double Eye Blinking Classification
0
Deep Learning

## Slide 79: Double Eye Blinking Classification
conv2D
conv2D
pooling
conv2D
Fully Connected Layers
0
Deep Learning

## Slide 80: Double Eye Blinking Classification : Feature Maps
0
Deep Learning

## Slide 81: Double Eye Blinking Classification : Feature Maps
0
Deep Learning

## Slide 82: Confusion Matrix
 | ACC | PRED | SEN
Class 0 | 98.07% | 97.44% | 99.78%
Class 1 | 98.07% | 99.75% | 97.11%
0
Deep Learning

## Slide 83: Left / Right Eye Blinking Classification
0
Deep Learning

## Slide 84: Left / Right Eye Blinking Classification
0
Deep Learning

## Slide 85: Left / Right Eye Blinking Classification
conv
conv
pooling
conv
conv
pooling
Fully Connected Layers
0
Deep Learning

## Slide 86: Left / Right Eye Blinking Classification : Feature Maps
0
Deep Learning

## Slide 87: Left / Right Eye Blinking Classification : Feature Maps
0
Deep Learning

## Slide 88: Left / Right Eye Blinking Classification
 | ACC | PRED | SEN
Class 0 | 95.23% | 98.83% | 98.60%
Class 1 | 95.23% | 97.14% | 95.78%
Class 2 | 95.23% | 95.57% | 97.07%
0
Deep Learning

## Slide 89
Chair
Hardware
Human brain
Streaming Data
Server
Decision
(Normal , forward ,
right , left)
MC
Control
Signal processing
Split
blinks
ML

## Slide 90
Introduction
Using microcontroller Esp32

## Slide 91: What is the difference Esp32&Esp8266?
Esp32 | ESp8266 | Features
2016 | 2014 | Release year
Xtensa dual-core 32bit | Xtensa single-core 32 bit | Microcontroller
Up to 240MHZ | 80 MHZ | Clock frequency
ULP | × | Co-processor
✓ | ✓ | Wi-Fi
520KB | 160KB | SRAM
✓ | × | Bluetooth
25 | 13 | GPIO
15 | 1 | ADC
2 | × | DAC

## Slide 92: How to build a server?
Connection modes :
  SOCK_DGRAM (UDP)
    Connection less
    Unreliable
  SOCK_STREAM (TCP)
    Connection orianted
    Reliable
Server

## Slide 93: Building server
Socket
IP
Server
port
Handle Client
Thread
Client1
Start

## Slide 94: Client attributes
Host IP
  A computer data network assigns a number called an Internet Protocol (IP) address to every computer and device connected to it.
Port address
  Every computer and mobile device runs many different internet-based apps, including email, web browsers and cloud storage drives. Each of these applications has one or more network “ports” assigned to it.

## Slide 95: How Esp32 Works as a Client?
Wi-Fi
IP
port
Setup
Left
Forward
Right
Backward
Stop
Client
loop
1
2
3
4
5

## Slide 96: Testing Car model
ESP32 with DC Motor and L298N Motor Driver Control Speed and Direction.

## Slide 97: Wheelchair Components
Aluminum body
Two Power window DC motors
Battery 12 V – 9 Amp
Two bike Wheels 16″
Cytron Dual Channel 10A DC Motor Driver
--

## Slide 98: Cytron Motor Driver Features
Bi-directional control for 2 brushed DC motor
Support motor voltage ranges from 5V to 30V
Maximum current up to 10A continuous and 30A peak for each channel
Speed control PWM frequency up to 20KHz
2 activation buttons for fast test on each channel

## Slide 99: Wheelchair Simulation
(Simulation1.1)